## Slide 1
A Short Survey at the Intersection of Reliability and Security in Processor Architecture Designs
By Louis Marriage, Freddie Sethi, Benjamin Hodgkins, Kwan Ho Lin

## Slide 2: Introduction
The importance of the topic – Kwan Ho Lin
Main contributions of the paper – Louis Marriage and Freddie Sethi
Conclusion – Benjamin Hodgkins

## Slide 3: Why is the topic important?
Learn a basic principle of ECCs for protecting data.
Give some common ways to improve system security by ECCs.
Learn how ECCs prevent data from being distorted by random errors.
Know about different security processor architecture

## Slide 4
ECC-based Reliable Processor Design

## Slide 5: ECC-based Reliable Processor Design
Random Error Correction
Data initially encoded before being stored
Corrupted by errors
Eventually passed through a decoding function
Figure 1 shows the formula data goes through when using random error correction

## Slide 6
ECC-based Reliable Processor Design
Data Regeneration
Similar to Random Error Correction
Not corrupted by errors
Part of the data is missing
Passed through a function to restore lost data

## Slide 7
ECC-based Reliable Processor Design
Self-Checking Checkers
Data fed through a function
Function runs alongside the main formula
Decoding function at the end
Final function checks whether it needs to decode the data or simply verify it
Figure 2 shows the formula used for self-checking checkers

## Slide 8: Architectural Vulnerability Factors (AVFs)

## Slide 9: Architectural Vulnerability Factors (AVFs)
Click to add text
Statistical Fault Injection
Method where errors are injected
Compared to model without errors
Computes AVF using mismatches and dividing by number of injected errors

## Slide 10
Architectural Vulnerability Factors (AVFs)
Little's Law
Uses Architecturally Correct Execution (ACE) bits
Intel defines ACE bits as bits within a system that affect the output of a program
Function takes the average bandwidth per cycle and average latency a bit in the architecture and subscript of ACE before multiplying together and dividing by the average number of bits inside the architecture
Formula used to calculate AVFs using Little's Law

## Slide 11
Architectural Vulnerability Factors (AVFs)
ACE Analysis in Performance Models
Uses performance model
Tries to determine which bits are ACE and which are un-ACE
Assumes that all bits are ACE until proven otherwise

## Slide 12: MIT Aegis Secure Processor
Four processing modes
Standard (STD)
Suspended Secure Processing (SSP)
Tamper-Evident (TE)
Private Tamper- Resistant (PTR)
STD and SSP are the lowest privilege mode which has no access to private memory
TE has read/write access to verified memory and a subset of security functions. PTR mode is the most privileged due to its access to PUF instructions
The off-chip protection uses Integrity verification(IV) and Memory Encryption(ME)
Can defend against a wide range of attacks
The PUF can also not be duplicated
Aegis can provide a strong defense with negligible overhead in gate size and performance
Figure 1 illustrates the model upon which Aegis is built. Basically, all trusted components are contained in a single-chip secure processor, which includes all security features and secret keys.

## Slide 13: Apple Secure Enclave Processor (SEP)
First introduced with the A7 processor and iPhone
Application processor(AP) and the Secure Enclave Processor (SEP)
Uses a KF filter
Encrypted in this format - AES-ECB, AES-CBC and AES-XEX

## Slide 14: Apple Secure Enclave Processor (SEP)
Built-in services which use the SEP
Unlock of device or account (Password & Biometric) – apple pay / verify passwords
Hardware Encryption/Data Protection/File Vault (Data-at-Rest)
Secure Boot (Firmware and OS Trust and Integrity)
Hardware control of camera (FaceTime)
Hardware number generation
SEP uses logical walls between software and security functions
The SEP uses a Unique ID for each separate device

## Slide 15: ARM TrustZone technology
Uses a single core with Two logical zones – secure world and non-secure world
Implementation Defined Attribution Unit (IDAU)
Security Attribution Unit (SAU)
Uses a Secure Gateway(SG) instructions
You can only access information if necessary
How ARM TrustZone technology is isolated
Software logic-based isolation
Traditional logic-based isolation
Obfuscated isolation
System hardware-based isolation
Discrete Sub-system isolation

## Slide 16: IBM 4765 Secure Processor
Placed on a PCLe card
Formats the data into cryptographic algorithms such as SHA-256, HMAC, and RSA
Uses a tamper-proof storage system which meets the 1402-2 level 4 security requirements
Checks for temperature changes or voltage spikes to see if the processor is functioning properly
The IBM 4765 hardware performs AES, DES, T-DES, SHA-1, SHA-256, MD5, HMAC and public key cryptographic algorithms, a secure clock/calendar, and a hardware random number generator
Uses Miniboot for the software side of security

## Slide 17: Intel Trusted Execution Technology (TXT)
Started shipping in 2010
By 2012, most major manufacturers offered Intel TXT–capable server platforms
A set of hardware extensions for the processors and chipsets
Hardware-based mechanisms help attacks against the software
Uses the Trusted Platform Module (TPM)
Two types of trust: the static chain and dynamic chain
Authenticated Code Module(ACM)
TXT works in launch-time

## Slide 18: Conclusion
In the conclusion, they reminisce on the both the reliable and the security-aware processor architectures. The reliable architectures are shown to strong against errors with its application of error correction protection to help stop random and limited errors. However, for the security-aware architectures it is a lot more entangled. This is because of they have different security demands and attack models for each of the designs that are on the market.

## Slide 19: References
Article title: PCIeCC 4765 Overview
Website title: Ibm.com
URL: https://www.ibm.com/security/cryptocards/pciecc/overview
Article title: What is Arm TrustZone Technology? - Hardware Based Isolation, TrustZone
Website title: Trustonic
URL: https://www.trustonic.com/technical-articles/what-is-trustzone/
Article title: Csg.csail.mit.edu
URL: http://csg.csail.mit.edu/pubs/memos/Memo-489/memo-489.pdf
Article title: People.csail.mit.edu
URL: https://people.csail.mit.edu/devadas/pubs/aegis-istr-august6-2005.pd
Author: Killian Bell
Article title: Apple's impenetrable security chip is penetrated by hacker
Website title: Cult of Mac
URL: https://www.cultofmac.com/498228/apples-impenetrable-security-chip-is-penetrated-by-hacker/
Article title: Security certifications for SEP: Secure Key Store
Website title: Apple Support
URL: https://support.apple.com/en-gb/HT209632
Website title: Fundamental Principles of Intel® TXT
URL : https://link.springer.com/chapter/10.1007/978-1-4302-6149-0_2